Top of Form

## Dimensions PC50MR-2

A. Overall length 18'3" 5550 mm B. Overall width 6'5" 1960 mm C. Overall height 8'7" 2625 mm D. Tail swing radius 3'6" 1060 mm E. Crawler length 8'3" 2520 mm F. Track gauge 5'1" 1560 mm G. Track shoe width 15.7" 400 mm H/I. Boom swing angle LH85/RH50 J/K. Bucket offset LH630/RH880 LH2'1"/RH2'11"

*Load is limited by hydraulic capacity rather than tipping. Rated loads do not exceed 87% of hydraulic capacity or 75% of tipping load.

Top of Form

## Working Range (Long Arm)

a. Max. digging height 20'5" 6215 mm b. Max. dumping height 14'9" 4495 mm c. Max. digging depth 13'8" 4160 mm d. Max. vertical digging depth 11'1" 3380 mm e. Max. digging reach 21'7" 6570 mm f. Max. digging reach at ground level 21'1" 6430 mm g. Min. swing radius 7'10" 2380 mm g. Min. swing radius (When boom swing) 6'0" 1840 mm h. Max. blade lift 1'5" 430 mm i. Max. blade depth 1'1" 330 mm

*Load is limited by hydraulic capacity rather than tipping. Rated loads do not exceed 87% of hydraulic capacity or 75% of tipping load.

Bottom of Form

Bottom of Form